## Slide 1: Cloud Engineering
Networking

## Slide 2: Overview
Recall from the devops course
Main network & subnets
Connecting to internet: gateways
DNS
Frontal services
Load balancing
CDN / 5G edge content deployment

## Slide 3: Topology
Networks are organized with routers and switches
Routers link together 2 networks (or more) OSI level 3
Switches link together devices in a same network OSI level 2
Recall from Devops course
Excellent learning material: Network Chuck’s Free CCNA Course

## Slide 4: Network Interface CarD
A NIC carries its own unique MAC address like 07:27:2d:40:83:gg (OSI level 2)
The MAC is mapped from an IP thanks to the ARP resolution
NICs are virtual in the cloud, VMs can have many attached
Recall from Devops course

## Slide 5: An IP is a number, within a RANGE
A serie of 32 bits
IPs that share the first N bits are part of a same network
The DHCP server assigns IPs to the connected devices, the new IP is within the defined network
Recall from Devops course
CIDR Notation:
10.20.30.0/24 network of all IPs starting with 10.20.30 ➡️24 common bits, 8 specific bits = 256 devices
10.20.30.1 is the default gateway IP, 10.20.30.255 is the broadcast IP

## Slide 6: Networks organisation
High level networks contain a large number of IPs: /16 CIDR
They can be peered to external networks for network to network communication
Have high level firewalling
AWS: Virtual Private Cloud VPC, Azure: Virtual Network VNet, OCI: Virtual Cloud Network VCN
Subnets are contained in the high level networks
Have low level firewalling
Gather resources working closely
VPC 1.2.0.0/16
Subnet 1.2.1.0/24
Subnet 1.2.2.0/24

## Slide 7: Private & public subnets
Internet Gateway allows instances to access the internet (same as the box wire to the ISP)
Public subnet = being connected to an IG
NAT Gateway = intermediate between instances in private subnets and an IG
Source: uturndata.com

## Slide 8: Complete route to internet
VM (EC2 instance)
Security group: acts as a firewall @VM level
Access Control Lists: act as a firewall @subnet level
➡️ Exit the subnet
(optional) Other subnet (if NAT)
Route table: tells who handles the traffic next
Internet Gateway
Example of AWS
Source: medium.com/awesome-cloud

## Slide 9: Ingress & Egress TRAFFIC
Relative to a subject: region, AZ, subnet, …
Ingress is typically free (AWS, Azure)
Egress is billed (€/GB) This includes traffic within an account, from one region to another
Rule of thumb: the farthest the more expensive but… complex pricing
Region
Source: https://azure.microsoft.com/en-us/pricing/details/bandwidth
INGRESS
EGRESS
North – South traffic
East – West traffic
VM
VM

## Slide 10: Virtual Private NetworkS
For hybrid clouds, connect the Cloud to on-premise (Site-to-Site S2S)
  AWS Site-to-Site VPN
  Azure VPN Gateway
  Needs a dedicated machine on the other end, on-premise
To secure a remote worker / single machine connection to the VPC (Point-to-Site P2S)
  AWS Client VPN
  Azure VPN Gateway (again)
Source: https://learn.microsoft.com
Cloud
Internet
On-prem

## Slide 11: DNS
1 owner purchases a domain name
The money is shared
  ICANN (assigns IP ranges to countries)
  the registry (manages a Top Level Domain database: .fr, .com, …)
  the registrar (shopping platform for domain names)

## Slide 12: DNS
Configuration of your domain name and subdomains
Setting of the records
  “A” record maps a name to an IPv4
  “CNAME” record maps a name to another name
Used to verify a domain ownership before certificate issuance for HTTPS
Can perform Load Balancing
AWS Route 53 & Azure DNS offer similar functionalities
Load balancing modes of OCI DNS

## Slide 13: Frontal security services
Load balancing and securing the VPC
Route53 DNS service
Shield Protects against DDoS attacks at the network edge
CloudFront Reverse-proxy to optimize and cache traffic for global distribution Can perform TLS offload
WAF Reverse-proxy to filter traffic for application-level (layer 7) security ex: blocks requests looking like SQL injection
API Gateway Reverse-proxy to dispatch requests to the right service
Example of AWS
INGRESS
Shield
DNS
Cloud Front
WAF
API Gateway
Internet Gateway

## Slide 14: Tour of the existing network resources
✨ Live demo in depth tour
Set up by default

## Slide 15: Architectural tip
Keep the network structure simple and understandable
Use firewalls to allow only intended inbound traffic
  all the rest should be closed
  possible strict IP whitelisting for services like SSH
Delegate TLS to a frontal service
Reduce the risks due to exposing VMs directly to internet by using a NAT Gateway
For a modest OCI setup